## Slide 1: ECE 2504: Introduction to Computer Engineering
Section 1:
Digital Systems and Information

## Slide 2: Introduction
Information in a computer system is stored in memory devices called registers.
  The information is typically stored as words.
  Information can be data words or control words. (What’s the difference?)
In this section, we will study:
  Data representation in computer systems.
  The impact of data representation on computer use and design.

## Slide 3: Number Systems
We define a number system by the radix r that it employs. Another name for the radix is the base.
  We represent a number using a string of symbols called digits.
  Each digit is weighted by an appropriate power of the radix.

## Slide 4: Number Systems
  For radix r, the n-digit integer:
  Xn-1 Xn-2 … X2 X1 X0
  has a value of:
  (Xn-1  rn-1) + (Xn-2  rn-2) + … + (X2  r2) + (X1  r1) + (X0  r0)
Example
The decimal (radix-10) integer 2504 has the value:
(2  103) + (5  102) + (0  101) + (4  100)

## Slide 5: Number Systems
  Digits to the right of the radix point are weighted using negative integral powers of the radix.
Example
The decimal (radix-10) fraction .1875 has the value:
(1  10-1) + (8  10-2) + (7  10-3) + (5  10-4)

## Slide 6: Binary Representation
Computer systems use binary as their primary data representation format
  The radix of the binary system is 2.
  Symbols: 0 (off, low, false, 0 volts) and 1 (on, high, true, 5 volts).
  Digital systems use binary because of hardware constraints. It is easier to implement systems where transistors are either turned off or fully saturated (on).

## Slide 7: Binary Representation
The digits of a binary number have weights that are powers of 2:
Example The number shown above has the value:
  256 + 32 + 8 + 4 + 2 + 0.5 + 0.25 + 0.0625 = 302.8125
It will be useful for you to learn the decimal equivalents of the positive integral powers of 2.
0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | . | 1 | 1 | 0 | 1
1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 |  | 1/2 | 1/4 | 1/8 | 1/16

## Slide 8: Base Conversion
As the previous slide shows, converting from binary to decimal is straightforward. Sum the weights that correspond to the non-zero bits.
We can convert from decimal to binary by two methods
  Decomposition
  Integer division and fraction multiplication

## Slide 9: Decimal-to-Binary Conversion
Decomposition
  Find the largest power of 2 that is less than or equal to the number.
  Subtract that power of 2 from the original number to find a new number
  Repeat these steps until you reach zero.
  Form the binary number using the powers of 2.
(137.4253)10 = ?

## Slide 10: Decimal-to-Binary Conversion
Integer Division
  Divide the number by 2. Record the remainder and preserve the integer quotient as the new number.
  Repeat the previous step until you reach zero.
  Assemble the remainders as the binary number in the opposite order that you derived them.

## Slide 11: Decimal-to-Binary Conversion
Example
Convert (137)10 to binary.
137/2 = 68 remainder 1
68/2 = 34 remainder 0
34/2 = 17 remainder 0
17/2 = 8 remainder 1
8/2 = 4 remainder 0
4/2 = 2 remainder 0
2/2 = 1 remainder 0
1/2 = 0 remainder 1
(137)10 = (10001001)2

## Slide 12: Decimal-to-Binary Conversion
Fraction Multiplication
  Multiply the fraction by 2. Record the integer result and preserve the fractional part as the new fraction
  Repeat the previous step until you reach zero, realize that the binary fraction will repeat, or run out of bits to represent the result.
  Assemble the integers as the binary fraction in the order that you derived them.

## Slide 13: Decimal-to-Binary Conversion
Example
Convert (0.4253)10 to binary.
0.4253  2 = 0.8506
0.8506  2 = 1.7012
0.7012  2 = 1.4024
0.4024  2 = 0.8048
0.8048  2 = 1.6096
0.6096  2 = 1.2192
0.2192  2 = 0.4384
0.4384  2 = 0.8768
(0.4253)10 ≈ (0.01101100)

## Slide 14: Octal Representation
The octal representation has radix 8.
The octal representation needs 8 symbols. We use the digits 0 to 7, inclusive
Since 8 = 23, 1 octal digit corresponds to 3 bits. This fact makes octal conversion easy.

## Slide 15: Binary-to-Octal Conversion
To convert from binary to octal, start at the radix point and move outward in both directions. Form groups of three bits and assign the equivalent octal digit to each group.
If a group has fewer than three bits, pad it with zeros on the extreme end.

## Slide 16: Binary-to-Octal Conversion
Example
Convert (10111011000.0011101)2 to octal.
(10111011000.0011101)2 = (2730.164)8
ALWAYS group from the radix point out in both directions.
010 | 111 | 011 | 000 | . | 001 | 110 | 100
2 | 7 | 3 | 0 | . | 1 | 6 | 4

## Slide 17: Octal-to-Binary Conversion
To convert from octal to binary, start at the radix point and move outward in both directions. Expand each octal digit into three bits.
In general, you can drop the leading and lagging zeros in the binary number.

## Slide 18: Octal-to-Binary Conversion
Example
Convert (1236.754)8 to binary.
(1236.754)8 = (1010011110.1111011)2
1 | 2 | 3 | 6 | . | 7 | 5 | 4
001 | 010 | 011 | 110 | . | 111 | 101 | 100

## Slide 19: Hexadecimal Representation
The hexadecimal representation has radix 16.
With only 10 decimal digits, we use A, B, C, D, E, and F as additional digit symbols.
A = (10)10 B = (11)10 C = (12)10 D = (13)10 E = (14)10 F = (15)10
Since 16 = 24, 1 hex digit corresponds to 4 bits. This fact makes hexadecimal conversion easy.

## Slide 20: Binary-to-Hexadecimal Conversion
To convert from binary to hexadecimal, start at the radix point and move outward in both directions. Form groups of four bits and assign the equivalent hexadecimal digit to each group.
If a group has fewer than four bits, pad it with zeros on the extreme end.

## Slide 21: Binary-to-Hexadecimal Conversion
Example
Convert (10111011000.0011101)2 to hex.
(10111011000.0011101)2 = (5D8.3A)16
ALWAYS group from the radix point out in both directions.
There are a number of common ways to represent the fact that a number is in hexadecimal.
0101 | 1101 | 1000 | . | 0011 | 1010
5 | D | 8 | . | 3 | A

## Slide 22: Hexadecimal-to-Binary Conversion
To convert from hexadecimal to binary, start at the radix point and move outward in both directions. Expand each hexadecimal digit into four bits.
In general, you can drop the leading and lagging zeros in the binary number.

## Slide 23: Hexadecimal-to-Binary Conversion
Example
Convert (29E.F6)16 to binary.
(29E.F6)8 = (1010011110.1111011)2
2 | 9 | E | . | F | 6
0010 | 1001 | 1110 | . | 1111 | 0110

## Slide 24: Binary Arithmetic
Addition – Add 1-bit addends x and y to obtain a 1-bit sum and a 1-bit carry to the next column.
Example
x | y | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
 | 1 | 1 | 0 | 1
+ | 0 | 1 | 0 | 1

## Slide 25: Binary Arithmetic
Subtraction – Subtract 1-bit subtrahend y from 1-bit minuend x to obtain a 1-bit difference and a 1-bit borrow from the next column.
Example
x | y | Difference | Borrow
0 | 0 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
 | 1 | 0 | 1 | 1
 | 0 | 1 | 0 | 1

## Slide 26: Binary Arithmetic
Multiplication – Use the long method to multiply an n-bit multiplicand by an n-bit multiplier. In general, a 2n-bit product results.
Example
 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1

## Slide 27: Binary Arithmetic
Division – Use the long method to divide a dividend by a divisor to obtain a quotient.
Example
1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 0

## Slide 28: Binary Numbers and Binary Coding
Flexibility of representation
  Within certain constraints, we can assign any binary combination (called a code word) to any data, as long as data is uniquely encoded.
Information Types
  Numeric
    Must represent range of data needed
    Very desirable to represent data such that simple, straightforward computation for common arithmetic operations permitted
    Tight relation to binary numbers
  Non-numeric
    Greater flexibility since arithmetic operations not applied.
    Not tied to binary numbers

## Slide 29: Binary-Coded Decimal
Binary-coded decimal (BCD) is an alternate representation for radix-10 numbers that uses binary.
To express a decimal number in BCD, represent each digit of the decimal number as a 4-bit binary value.
Example
(948)10 = (1001 0100 1000)BCD
(2504)10 = (0010 0101 0000 0100)BCD

## Slide 30: Binary-Coded Decimal
Problems with BCD
  Inefficient coding: We can use 4 bits to represent 16 different numbers. BCD only uses 10 of them.
  Arithmetic: Sometimes we must correct arithmetic that uses BCD.

## Slide 31: Non-numeric Binary Codes
Given n binary digits (called bits), a binary code is a mapping from a set of represented elements to a subset of the 2n binary numbers.
Example: A binary code for the seven colors of the rainbow
Code 100 is not used
Color | Binary Number
Red | 000
Orange | 001
Yellow | 010
Green | 011
Blue | 101
Indigo | 110
Violet | 111

## Slide 32: How Many Bits Does a Particular Mapping Need?
Given M elements to be represented by a binary code, the minimum number of bits (n) needed satisfies the following:
if 2(n – 1)  M < 2n → n = log2 M
x is the ceiling function. The ceiling of x is the integer greater than or equal to x.
Think back. How many bits are required to represent decimal digits with a binary code?
Notes: M = 10
Therefore n = 4 since:
24 =16 is  10 > 23 = 8
and the ceiling function for log2 10 is 4.

## Slide 33: How Many Elements Can Be Mapped?
Given n digits in radix r, there are rn distinct elements that can be represented.
However, you can also represent m elements such that m is less than rn
Examples:
  You can represent 4 elements in binary with n = 2 bits: (00, 01, 10, 11).
  You can represent 4 elements in binary with n = 4 bits: (0001, 0010, 0100, 1000).
  This second encoding is called a "one hot" code.

## Slide 34: Other Binary Codes
Gray Code
  The standard order of counting is such that multiple bits may change between consecutive codes.
  In Gray code, one and only one bit changes between consecutive codes.
  Example The standard 3-bit Gray code is 000 – 001 – 011 – 010 – 110 – 111 – 101 – 100.

## Slide 35: Other Binary Codes
Excess-n
  Prior to expressing a number, we can add an offset and use the code for the resulting value as the code for the original number.
  For example, in an excess-3 BCD representation, the code for 0 is 0011, because 0 + 3 = 3, and 3 has the representation 0011 in BCD.

## Slide 36: Other Binary Codes
Uses of Excess-n
  Excess-3 BCD representation also eases certain aspects of BCD arithmetic.
  IEEE 754 floating point uses excess-127 (for single precision) and excess-1023 (for double precision) to represent its exponents.

## Slide 37: Other Binary Codes
ASCII – American Standard Code for Information Interchange
  ASCII represents one method of assigning binary codes to alphanumeric, punctuation, and special characters.
  There are 128 standard ASCII characters. This would normally require 7 bits of encoding.
  Extended ASCII uses an eighth bit to add 128 characters.
  http://www.asciitable.com/

## Slide 38: Other Binary Codes
Error Detection Codes
  The simplest approach to error detection is to add a parity bit to a transmitted word.
  We add a bit to an n-bit word such that the total number of ones – including the parity bit – is even (even parity) or odd (odd parity)
  The receiver checks the parity of the received word and somehow acts in accordance with the judgment of the parity checker.

## Slide 39: 4-Bit Parity Code Example
Message plus even parity bit | Message plus odd parity bit
000_ | 000_
001_ | 001_
010_ | 010_
011_ | 011_
100_ | 100_
101_ | 101_
110_ | 110_
111_ | 111_
Fill in the even and odd parity bits:
The complete code word "1111" has even parity and the codeword "1110" has odd parity. Both can be used to represent 3-bit data.

## Slide 40: Terms of Use
Portions of this material © 2008 by Pearson Education, Inc.
Permission is given to incorporate this material or adaptations thereof into classroom presentations and handouts to instructors in courses adopting the latest edition of Logic and Computer Design Fundamentals as the course textbook.
These materials or adaptations thereof are not to be sold or otherwise offered for consideration.
This Terms of Use slide or page is to be included within the original materials or any adaptations thereof.