## Slide 1: ECE 2504: Introduction to Computer Engineering
Section 7:
Memory (Chapter 8)

## Slide 2: Memory: Organization & Characteristics
Memory is a collection of registers, along with the logic needed to access them.
  The collection of registers that forms the general storage area of a memory chip is called the Memory Unit.
Memory
Unit

## Slide 3: Memory: Organization & Characteristics
Memory is a collection of registers, along with the logic needed to access them.
  Each of the registers that comprises the Memory Unit has a unique binary identifier, which is called an address. (The term address is also applied to the registers themselves.)
Each of the white boxes represents one register of the Memory Unit. This Memory Unit has 2k registers.
Each register is shown having a decimal-valued address. Using k bits of information, we can represent any unsigned value from 0 to (2k – 1).
.
.
.
0
1
2
3
4
5
6
7
8
9
2k - 1

## Slide 4: Memory: Organization & Characteristics
Memory is a collection of registers, along with the logic needed to access them.
  Each of the registers in the Memory Unit can hold a particular amount of data. The amount of data is measured in bits.
Each of the black boxes represents one bit of Register 0. Like Register 0, each register of this Memory Unit contains m bits.
Each bit of a register represents a single flip-flop, although as we will see, one bit’s worth of information need not always be implemented using a flip-flop.
.
.
.
0 …
1
2
3
4
5
6
7
8
9
2k - 1
m - 1
3
2
1
0

## Slide 5: Memory: Organization & Characteristics
Example: Consider a 32K x 16 memory chip.
  This chip has 32,768 (or 215) registers. Each register can hold 16 bits of data.
  This Memory Unit has an address space of 32K and a data width of 16 bits.
  Since there are 8 bits in 1 byte, the capacity of the Memory Unit (in bytes) is: (32K addresses)  (2 Bytes per address) = 64 kilobytes, or 64 KB.
  Remember: We use metric prefixes to describe certain powers of two: 1K = 210, 1M = 220, 1G = 230, etc.
Memory
Unit
32K addresses
16 bits per address

## Slide 6: Memory: Operation
Memory operations come in two varieties:
  In a memory read, we want to extract information from a specific register of the Memory Unit. The Memory Unit register is the source of the information.
  In a memory write, we want to place a piece of information into a specific register of the Memory Unit. The Memory Unit register is the destination of the information.
In both cases, we must identify one of the registers to be the source of a read or the destination of a write uniquely. Any of the registers could be the source or the destination, but only one register can do so at a time.
To accomplish all of this, we must account for a number of different inputs and outputs. Let’s consider a memory chip having 2k registers. Each of the registers holds m bits.

## Slide 7: Memory: Operation
Address lines
  To choose a unique register from among 2k registers, we need k bits of address information.
  This information is carried on the address lines of the memory chip.
Memory
Unit
k
Address lines

## Slide 8: Memory: Operation
Data lines
  To facilitate parallel data transfer both to and from the m-bit registers, we need m data lines.
  On most memory chips, the data lines are bidirectional, so they can serve as inputs during a memory write, and as outputs during a memory read.
Memory
Unit
k
Address lines
m Data lines

## Slide 9: Memory: Operation
Control lines
  To identify the times when a register is the source or destination of data, we need a read line and a write line. When the user asserts one of the lines, that operation is performed.
  To identify the times when we want the memory to be active (to be readable or writeable) or inactive, we need an enable line.
  A clock governs when the registers can change values
Memory
Unit
k
Address lines
m Data lines
Read
Write
Enable
Clock

## Slide 10: Memory: Components
A memory chip contains a number of components.
  Memory Unit: The collection of 2k m-bit registers.
Memory
Unit
k
Address lines
m Data lines
Read
Write
Enable
Clock

## Slide 11: Memory: Components
A memory chip contains a number of components.
  Memory Address Register (MAR): A register that holds the value provided by the k address lines.
  The MAR is a k-bit register.
  MAR is effectively a “pointer”: The value contained in MAR is the address of the Memory Unit register we wish either to read or to modify.
MAR
Memory
Unit
k
Address lines
m Data lines
Read
Write
Enable
Clock

## Slide 12: Memory: Components
A memory chip contains a number of components.
  Decoding circuitry: A k-to-2k decoder takes the k outputs of MAR and generates 2k outputs.
  Each of the 2k decoder outputs acts as a enable input for one of the 2k registers of the Memory Unit.
  Only the register that is enabled will be able to supply its value in the case of a memory read, or accept a new value in the case of a memory write.
  Disabled registers do not play a role in read or write operations.
MAR
Decoder
Memory
Unit
k
Address lines
m Data lines
Read
Write
Enable
Clock
k
2k

## Slide 13: Memory: Components
A memory chip contains a number of components.
  Memory Data Register (MDR): A register that holds data that is on its way into out of a register in the case of a read, or on its way into a register in the case of a write.
  The register in the Memory Unit that has been enabled by the decoder will place its value into MDR on a read, or will take in the value of MDR as its new value in the case of a write.
  The MDR is an m-bit register.
MAR
Decoder
Memory
Unit
MDR
k
Address lines
m Data lines
Read
Write
Enable
Clock
k
2k
m

## Slide 14: Memory: Components
A memory chip contains a number of components.
  Control circuit: The control circuit uses the read and write inputs to control the direction of the data lines.
  It uses the enable input to enable and disable the memory unit as a whole. One way to do this is by enabling and disabling the decoder. If the decoder is disabled, then none of the registers in the memory unit are enabled, regardless of what the value on the address lines might be.
MAR
Decoder
Memory
Unit
MDR
k
Address lines
m Data lines
Control Circuit
Read
Write
Enable
Clock
k
2k
m

## Slide 15: Memory: Components
A memory chip contains a number of components.
  Clock circuitry: The clock circuitry provides clock signals for all of the registers in the memory chip.
  This includes the registers in the Memory Unit, the MAR, and the MDR.
  Synchronizing all of the registers prevents sudden input changes from disturbing the operation of the memory chip.
MAR
Decoder
Memory
Unit
MDR
k
Address lines
m Data lines
Control Circuit
Read
Write
Enable
Clock
k
2k
m
Clock Circuitry

## Slide 16: Memory: Register Transfers
We can express memory read and memory write operations as a sequence of register transfers.
Some of the registers involved in the transfers will be those of the memory chip, while others could be general-purpose or specific purpose registers elsewhere in the system.
Memory Write: Store the contents of (external) register R1 at memory address 0x100
  MAR  0x100 Place the address into the memory address register.
  MDR  R1 Move the value in R1 to the memory data register.
  Mem[MAR]  MDR Write the contents of MDR (which is the value in R1 that we want to store) to the Memory Unit register whose address is given by the value in MAR.

## Slide 17: Memory: Register Transfers
Memory Read: Load (external) register R1 with the contents of memory address 0x100:
  MAR  0x100 Place the address into the memory address register.
  MDR  Mem[MAR] Read the contents of the Memory Unit register whose address is given by the value in MAR and place the value into MDR.
  R1  MDR Move the value in MDR (which is the value that was read from memory) to register R1.

## Slide 18: IC Random Access Memory
A memory’s access time is the amount of time that it takes to access a storage location.
Random access memory (RAM) is characterized by the ability to access a random (or arbitrary) storage location with constant access time. The storage locations (the registers) need not be accessed in order by their location in memory (their address).
  RAM is contrasted with sequential access memory, where the access time is dependent upon the storage location. Accessing two different storage locations in a SAM can take different amounts of time. Examples of SAM include hard drives and magnetic tape drives.
RAM is an example of volatile memory: RAM only retains its contents for as long as it is powered. When power is discontinued, the storage locations lose their values.
RAM comes in two categories: static RAM (SRAM) and dynamic RAM (DRAM).

## Slide 19: IC RAM: Static RAM
SRAM is organized in cells that are built around flip-flops.
  Each cell represents one bit of one register.
  The bits in SRAM retain their values for as long as the memory chip is powered.
  Compared to DRAM, SRAM is faster but is more expensive.

## Slide 20: IC RAM: Dynamic RAM
DRAM is organized around transistor-capacitor pairs.
  Each capacitor represents one bit.
  The transistors provide pathways that allow a capacitor to be charged or discharged (to change its value) or prevent it from charging or discharging (to hold its value).
  Because the transistors leak even when they are not conducting and the capacitors have a tendency to discharge, DRAM must be refreshed periodically.
  Compared to SRAM, DRAM is slower but less expensive.

## Slide 21: IC Read-Only Memory
Read-only memory (ROM) is a version of RAM that (in general) can only be read.
  ROM is used for “permanent” data storage.
  Information is “written” to the ROM as part of the memory’s production process.
  Once the ROM has been fabricated, the device is read-only.
  In contrast to RAM, which is volatile, ROM is non-volatile: it does not lose its contents when power is discontinued. ROM’s non-volatility stems from the fact that the “memory” is stored through the connections that are made between circuit elements; these connections don’t go away when the chip is not powered.
  A 2k-by-m ROM uses its k address lines to provide an m-bit data output.

## Slide 22: IC ROM: Varieties of ROM
Variations on ROM allow field-programmability, and even re-programmability.
  Field Programmable Read-Only Memory (PROM): Instead of being fabricated industrially, a PROM is programmable by an end user.
  Erasable Programmable Read-Only Memory (EPROM): EPROM is electrically-programmable. The devices that make up an EPROM store charge to represent logic values. The devices are not susceptible to charge leakage, but UV radiation can cause the charge to dissipate, which can erase the memory and allow for it to be reprogrammed.
  Electrically Erasable Programmable Read-Only Memory (EEPROM): EEPROM is electrically-programmable and – as the name suggests – electrically erasable. It is more versatile than EPROM insofar as it allows for more flexible erasure.
  Flash memory was developed from EEPROM. Modern computers use Flash to hold the firmware, but early generations of computers used PROM for this purpose; many subsystems and peripherals of contemporary computers still do.

## Slide 23: IC ROM: Programming
ROM is implemented as a combinational circuit
  The decoder inputs are the address inputs. Each of the decoder outputs represents one address of the ROM.
  Each of the OR-gate outputs represents one data output line.
Suppose that the diagram below shows an 8-by-4 PROM. It has three address inputs and four data outputs.
In its “unprogrammed” state, all of the words stored in the PROM are 1111
A2 | A1 | A0 | D3 | D2 | D1 | D0
0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 24: IC ROM: Programming
Programming the ROM requires breaking certain connections between the decoder outputs and the OR-gate inputs.
  In different varieties of ROM, this is done by breaking a fuse or by setting the state of an electronic switch, i.e., a transistor. In effect, this grounds the OR-gate input.
  Breaking the connection between decoder output Qj and the OR-gate whose output is Di writes a zero to bit i of word j.
  The broken connections are symbolized by crossed-out nodes.
A2 | A1 | A0 | D3 | D2 | D1 | D0
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1

## Slide 25: Memory Implementation
Suppose that we need of a memory space whose address space is 1K and whose data width is 16 bits, but we only have memory chips whose address space is 1K and whose data width is 8 bits.
Each of our memory chip has 10 address lines and 8 data lines. The memory space that we want requires 10 address lines and 32 data lines.
ADDR
DATA
R
CLK
W
EN

## Slide 26: Memory Implementation
If the data width of the memory space we are trying to implement is 32 bits and the memory chips have data widths of 8 bits each, then we need four memory chips to match the desired data width.
You should imagine that one 32-bit register of the desired memory space is being spread out over the four memory chips. If we have access to a 32-bit data bus…
ADDR
DATA
R
CLK
W
EN
ADDR
DATA
R
CLK
W
EN
ADDR
DATA
R
CLK
W
EN
ADDR
DATA
R
CLK
W
EN
DATA
32 (D31 – D0)

## Slide 27: Memory Implementation
Then we can split the bus and divide the data among the four memory chips.
Each memory chip is responsible for storing eight bits in one of its registers.
ADDR
DATA 8
(D31 – D24)
R
CLK
W
EN
ADDR
DATA 8
(D15 – D8)
R
CLK
W
EN
ADDR
DATA 8
(D23 – D16)
R
CLK
W
EN
ADDR
DATA 8
(D7 – D0)
R
CLK
W
EN
DATA
32 (D31 – D0)

## Slide 28: Memory Implementation
Since the address spaces of the memory chips are supposed to represent a set of “extra-wide” registers, we want a 10-bit address to choose the same register on each chip. We can tie a 10-bit address bus to the address buses of the four memory chips.
ADDR
DATA 8
(D31 – D24)
R
CLK
W
EN
ADDR
DATA 8
(D15 – D8)
R
CLK
W
EN
ADDR
DATA 8
(D23 – D16)
R
CLK
W
EN
ADDR
DATA 8
(D7 – D0)
R
CLK
W
EN
DATA
32 (D31 – D0)
ADDR
10 (A9 – A0)
10
(A9 – A0)
10
(A9 – A0)
10
(A9 – A0)
10
(A9 – A0)

## Slide 29: Memory Implementation
There is no room to show it in this diagram, but since all four chips are actually the same memory space, we should connect the four clocks together, the four Read lines together, the four Write lines together, and the four Enable lines together.
ADDR
DATA 8
(D31 – D24)
R
CLK
W
EN
ADDR
DATA 8
(D15 – D8)
R
CLK
W
EN
ADDR
DATA 8
(D23 – D16)
R
CLK
W
EN
ADDR
DATA 8
(D7 – D0)
R
CLK
W
EN
DATA
32 (D31 – D0)
ADDR
10 (A9 – A0)
10
(A9 – A0)
10
(A9 – A0)
10
(A9 – A0)
10
(A9 – A0)

## Slide 30: Memory Implementation
Now suppose that we need a memory space whose address space is 4K and whose data width is 8 bits. Once again, we have our 1K-by-8 memory chips.
Each of our memory chip has 10 address lines and 8 data lines. The memory space that we want requires 12 address lines and 8 data lines.
ADDR
DATA
R
CLK
W
EN

## Slide 31: Memory Implementation
If the address space of the memory space we are trying to implement is 4K and the memory chips have address spaces of 1K each, then we need four memory chips to match the desired address space.
This time, imagine that the address space is spread out over four memory banks. (Yes, that’s where we get the term!)
If we have access to a 12-bit address bus…
ADDR
DATA
R
CLK
W
EN
ADDR
DATA
R
CLK
W
EN
ADDR
DATA
R
CLK
W
EN
ADDR
DATA
R
CLK
W
EN
ADDR
12 (A11 – A0)

## Slide 32: Memory Implementation
Then we can use the lowest 10 bits of the address bus to control the address lines of all four memory chips in common. The lowest 10 bits are responsible for choosing the same address on each of the four banks.
However, in the end we only want one register to be active...
ADDR
DATA
R
CLK
W
EN
ADDR
DATA
R
CLK
W
EN
ADDR
DATA
R
CLK
W
EN
ADDR
DATA
R
CLK
W
EN
ADDR
12 (A11 – A0)
10
(A9 – A0)

## Slide 33: Memory Implementation
We can use the remaining two address lines as the inputs of a 2-to-4 decoder. The decoder outputs will choose a memory bank by enabling only one of the four banks and disabling the rest.
ADDR
DATA
R
CLK
W
EN
ADDR
DATA
R
CLK
W
EN
ADDR
DATA
R
CLK
W
EN
ADDR
DATA
R
CLK
W
EN
ADDR
12 (A11 – A0)
10
(A9 – A0)
A1 D0
A0 D1
D2
D3
A11
A10

## Slide 34: Memory Implementation
(In general, we need a decoder that has as many outputs as there are memory banks. In such an implementation, we will have enough leftover address lines from the bus to control the inputs of such a decoder.)
ADDR
DATA
R
CLK
W
EN
ADDR
DATA
R
CLK
W
EN
ADDR
DATA
R
CLK
W
EN
ADDR
DATA
R
CLK
W
EN
ADDR
12 (A11 – A0)
10
(A9 – A0)
A1 D0
A0 D1
D2
D3
A11
A10
(Bank 0)
(Bank 1)
(Bank 2)
(Bank 3)

## Slide 35: Memory Implementation
Since the memory space is supposed to represent one “extra-tall” set of 8-bit addresses, we want an 8-bit data bus to have equal access to the data buses of all 4 memory chips.
ADDR
DATA
R
CLK
W
EN
ADDR
DATA
R
CLK
W
EN
ADDR
DATA
R
CLK
W
EN
ADDR
DATA
R
CLK
W
EN
ADDR
12 (A11 – A0)
10
(A9 – A0)
A1 D0
A0 D1
D2
D3
A11
A10
(Bank 0)
(Bank 1)
(Bank 2)
(Bank 3)
DATA
8 (D7 – D0)

## Slide 36: Memory Implementation
There is no room to show it in this diagram, but since all four chips are actually the same memory space, we should connect the four clocks together, the four Read lines together, and the four Write lines together.
As you can see, we should not tie the four Enable lines together. They are separate because we need them to selectively enable the memory banks.
ADDR
DATA
R
CLK
W
EN
ADDR
DATA
R
CLK
W
EN
ADDR
DATA
R
CLK
W
EN
ADDR
DATA
R
CLK
W
EN
ADDR
12 (A11 – A0)
10
(A9 – A0)
A1 D0
A0 D1
D2
D3
A11
A10
(Bank 0)
(Bank 1)
(Bank 2)
(Bank 3)
DATA
8 (D7 – D0)

## Slide 37: Memory Implementation
We can apply both of the previous techniques to implement a memory space that is both “wider” and “taller” than the memory space provided by one memory chip.
Suppose that we wanted to implement a 4K-by-32 memory space using 1K-by-8 memory chips.
  The memory space requires 12 address lines and 32 data lines. Each of the chips requires 10 address lines and 8 data lines.
  The memory space would be equivalent to an “array” of 1K-by-8 chips; there would be 16 chips arranged into four rows and four columns.
  The memory space’s data bus would be split into four 8-bit divisions. Each column of chips would receive the same 8 bits of data from one of the four divisions.
  All 16 chips would receive the lowest 10 bits of the memory space’s address bus.
  The remaining two address lines would be the inputs of a 2-to-4 decoder. One decoder output would be tied in common to all of the chips in one row, with each row getting one of the four decoder outputs.

## Slide 38: Summary
Memory: Organization and Characteristics, Operation, Components, Register Transfers
Types of memory: RAM and ROM
Types of RAM: Static and Dynamic
Types of ROM: ROM, PROM, EPROM, EEPROM
Volatility vs. Non-Volatility
ROM Programming
Memory Implementation

## Slide 39: For Further Study
Volatile memory: RAM
  Static RAM
  Dynamic RAM
Non-volatile memory: ROM
  Programmable ROM
  EPROM
  EEPROM
  Flash Memory (Classified as “non-volatile RAM”)