## Slide 1: ECE 2504: Introduction to Computer Engineering
Assembly Language Programming for the Simple Computer

## Slide 2: First: The Instruction Set
Our computer is an example of a load-store architecture.
  The computer uses load and store instructions to move information between memory and registers.
  The majority of the instructions operate upon the values in registers.

## Slide 3: The Instruction Set
Instructions come in three types:
  Register instructions – In general, these instructions use one or two source registers as operands and a destination register to hold the result.
  Immediate instructions – In general, these instructions use one register and an immediate (a constant) as operands and a destination register to hold the result
  Jump and branch instructions – These instructions allow the computer to move non-linearly through its program memory.
Instructions in each type can be categorized further based on their function.

## Slide 4: Register Instructions
Register instructions exist that allow us to do a number of things:
  Arithmetic
    ADD RD, RA, RB SUB RD, RA, RB
    INC RD, RA DEC RD, RA
  Logic
    AND RD, RA, RB OR RD, RA, RB
    XOR RD, RA, RB NOT RD, RA
  Shift
    SHR RD, RB SHL RD, RB
  Data transfer
    LD RD, RA ST RA, RB
    MOVA RD, RA MOVB RD, RB

## Slide 5: Loading, Storing, and Moving
The LD instruction uses the value in Register A as a memory address. The value contained in that memory address is what is loaded into RD.
The ST instruction uses the value in Register A as a memory address. The value contained in RB is what is stored into that memory address.
The MOVA and MOVB instructions are register transfers. The value in RA (or RB) is what is moved into RD.

## Slide 6: Immediate Instructions
Immediate instructions use a constant value in the place of one of the register operands.
The immediate field replaces that field in the machine instruction. Since the field is only three bits wide, we can only use immediates between 0 and 7. (The computer zero-fills the immediate to obtain 16-bit values.)

## Slide 7: Immediate Instructions
Immediate instructions exist that allow us to do a “number” of things:
  Arithmetic
    ADI RD, RA, OP
  Data transfer
    LDI RD, OP

## Slide 8: Jump and Branch Instructions
Normally, the program counter increments after an instruction. This allows the computer to execute the next consecutive instruction.
Jump and branch instructions allow the computer to move to non-consecutive instructions.
As we will see, this is useful when writing things like IF-structures and FOR-loops.

## Slide 9: Jump and Branch Instructions
Jump and Branch instructions allow us to do a number of things:
  Unconditional Branch
  JMP RA – Jump to the program memory address specified by the contents of RA
  Conditional Branches
  BRZ RA, AD – If the value in RA = 0, branch to a location that is AD addresses from the current location. Else, continue to the next instruction.
  BRN RA, AD – If the value in RA < 0, branch to a location that is AD addresses from the current location. Else, continue to the next instruction.

## Slide 10: Say That Again?
This JMP instruction bases its destination on the value in a register.
This will make it more difficult to use than unconditional branches in other assembly instruction sets, especially because our instruction set does not support the use of labels.
Normally, this kind of thing would be handled by a compiler so that we wouldn’t have to get our hands dirty.
We’ll see a novel work-around; the moral of the story will be “If you’re actually writing assembly code, play the hand you’re dealt by the existing instruction set.”

## Slide 11: There’s More?
The branch instructions take a value as an offset.
Unlike the immediate values which are zero-filled and always represent positive numbers, the offset is sign-extended, and thus can represent positive or negative numbers.
Thus, a branch can reach a location that is between -32 and +31 instructions from the location of the branch.

## Slide 12: So How Does It All Come Together?
Let’s do some arithmetic!
// Put some numbers in some registers
LDI R0, 0
LDI R1, 4
LDI R2, 5
LDI R3, 2
// Seemingly random arithmetic!
ADD R4, R1, R2
ADD R5, R1, R3
SUB R6, R2, R1
SUB R7, R0, R3
What values do R4, R5, R6, and R7 contain at the end of the program?

## Slide 13: Bringing It Together
Writing code in assembly language is not really different than writing any other kind of code.
You have to know what the instructions in your instruction set are capable of doing.
You must be able to write an algorithm that will implement the behavior you want your program to do.
If the steps of your algorithm are sufficiently fine, then writing code will amount to translating your algorithm into code using the instructions in the instruction set.

## Slide 14: “Building” Large Immediate Values
If you think of what the number looks like in hexadecimal, you can construct it one hex digit at a time.
LDI R1, 2 ADI R1, 0
SHL R1, R1 SHL R1, R1
SHL R1, R1 SHL R1, R1
SHL R1, R1 SHL R1, R1
SHL R1, R1 SHL R1, R1
ADI R1, 5 ADI R1, 4
SHL R1, R1
SHL R1, R1
SHL R1, R1
SHL R1, R1
What should we do if a digit is greater than 7?

## Slide 15: Conditional Code Structures
The branch instructions allow us to move to another location contingent upon a register’s value.
We can use this to create IF-THEN-ELSE structures and FOR-loops (which fundamentally are applications of IF-THEN-ELSE structures).

## Slide 16: IF-THEN-ELSE
The BRZ allows us to jump to a location in the program contingent upon whether the value in some register equals zero.
Depending on the value, we can perform an arithmetic or logical operations on the value in some register that will produce a result that is either zero or non-zero.
The value of the resulting operation will tell us whether we should branch or not.

## Slide 17: Example #1
Is the value in register R1 = 2?
// Assume that R1 already has a value in it.
LDI R2, 2
SUB R3, R1, R2
// R1 – 2 = 0 if and only if R1 = 2. Thus, if the // test succeeds, we will jump to…?
BRZ R3, ?
// If the test fails, we execute the next line of // code, so we continue with the program
[Another line of code]

## Slide 18: What? You Mean I Have To Count?
What value should follow the register value in the BRZ instruction?
If our assembler used labels, we could label the destination of the branch and use that label in the branch instruction.
Our assembler doesn’t use labels, so the only thing we can do is count lines of code to figure out what the offset should be.
This means that if the code changes, it’s possible that the offset will need to change.

## Slide 19: Example #2
Is the value in register R1 equal to the value in register R2?
// Assume that R1 and R2 already have // values in them.
// How can we compare R1 and R2? Let’s say // that the result of the comparison should // go into R3.
??????
// What comes next?
??????
// What comes after that?
??????

## Slide 20: FOR Loops
A FOR loop must be built around an IF-THEN-ELSE structure.
Suppose that you want to execute a block of code k times.
Each time you complete the block of code, you must pose the following question – the phrasing here is intentional:
“IF I have executed the code block k times, THEN I should continue with the program, ELSE I should go back and execute the code block again.”

## Slide 21: FOR Loops
The FOR loop in assembly consists of two key elements:
  A FOR loop counter that (in some way) keeps track of how many times something has been done.
  An IF-THEN-ELSE structure that judges whether the the FOR loop counter has been exhausted.

## Slide 22: Example #1
Let’s carry out a block of code 10 times:
// At some point before the block of // code, initialize the counter.
LDI R1, 5
SHL R1, R1
// Do whatever you need to do.
[Block of code]
// Decrement the counter to indicate // that you have completed an iteration.
DEC R1, R1
(continued on the next slide)

## Slide 23: Example #1 (Continued)
// Now for the magic! Check the value of // R1. IF R1 = 0, THEN we have done the // block 10 times, and should continue // with the program. ELSE we should go // back and do the block of code all over // again.
BRZ R1, ?
JMP ?
[This line of code comes next.]
What value should we use for the address offset of the BRZ?
What should we do with the JMP instruction?

## Slide 24: Say That Again, Again?
If we know where we want to branch, we need only calculate the offset and insert that value into the instruction.
Labels would help with that, and it’s possible that a compiler or an assembler might do it for us, but at least we can do that for ourselves.

## Slide 25: Say That Again, Again?
For a JMP, we have to make sure that the destination address is in a register.
A compiler would normally do this for us as well, but this can be difficult to do for ourselves.
At the very least, it would involve writing the entire program, knowing what the destination address was, and finding a register to hold that value.
With limited registers and a limited capacity for generating immediates…no.

## Slide 26: Example #1, Modified
// Create a zero register.
XOR R0, R0, R0
// At some point before the block of code, // initialize the counter.
LDI R1, 5
SHL R1, R1
// Do whatever you need to do.
[Block of code]
// Decrement the counter to indicate that // you have completed an iteration.
DEC R1, R1
(continued on the next slide)

## Slide 27: Example #1, Modified (Continued)
// Check the value of R1.
BRZ R1, ?
BRZ R0, ?
[This line of code comes next.]
What value should we use for the address offset of the first BRZ?
Under what circumstances will the second BRZ succeed?
What value should we use for the address offset of the second BRZ?

## Slide 28: Making a “Jump Relative”
The second BRZ is now a relative jump.
Since we know that it will always succeed (in the case of our code, R0 = 0 always), the branch is unconditional, just like a regular JMP.
However, since the instruction is a branch instruction, we can specify an address offset instead of having to provide the destination address to a register.
Play the hand you’re dealt!