## Slide 1: ECE 2504: Introduction to Computer Engineering
Assembly Language, Function Calls, Compilers, and You

## Slide 2: Assemblers and Compilers
In general, a compiler is a program that translates another program written in a high-level language (like C) into a lower-level language (like assembly language).
In general, an assembler is a program that translates a program written in assembly language into machine language.
Having considered the process of machine code assembly, let’s look at specific examples of high-level language compilation.

## Slide 3: Function Calls
Procedures (functions) are one of the primary means of code re-use in high-level languages
E.g., in C:
Then elsewhere:
int my_function (int a, int b) {
int temp;
temp = 2*a + b;
return temp;
}
int main() {
...
variable1 = my_function(1,2);
...
...
variable2 = my_function(3,7);
...
...
}
“Caller”
“Callee”
Program returns here after first call
Program returns here after second call

## Slide 4: Steps in a Function Call
Caller prepares function parameters by copying them in a place where the callee expects to find them.
Caller transfers control to the callee.
Callee acquires storage resource.
Callee executes.
Callee places return values in a place where the caller expects to find them.
Callee returns control to the caller.

## Slide 5: Function Call Conventions
Typically the assembler/compiler will follow some convention about where values are placed, so that every function call will be set up the same way
Example:
  The first two function parameters will be in registers 1 and 2
  The return value will be in register 3
  The return address will be in register 0

## Slide 6: Function Call Example
Becomes the following in assembly:
int my_function (int a, int b) {
int temp;
temp = 2*a + b;
return temp;
}
// The address of mova // corresponds to MY_FUNCTION
// Fetch parameter a from r1. Use r4 // as a “scratchpad” register
mova r4, r1
// Multiply a by 2.
shl r4, r4
// Add b to 2a; b is in r2
add r4, r4, r2
// Put the function result into the // returned paramater address.
mova r3, r4
// Return to the main routine.
jmp r0

## Slide 7: Function Call Example
This:
becomes the following:
// Put the arguments into r1, r2.
ldi r1, 1
ldi r2, 2
// Put the return location into r0.
// But what do we do if RETURN1_LOCATION >7?
ldi r0, RETURN1_LOCATION
// Now make the function call.
// Again, what do we do if MY_FUNCTION > 7?
ldi r5, MY_FUNCTION
jmp r5
// Will return here: RETURN1_LOCATION.
ldi r4, VARIABLE1_LOCATION
// Variable1 value was returned in r3.
st r4, r3
// Set up the arguments for the second call // the same way
int main() {
...
variable1 = my_function(1,2);
...
...
variable2 = my_function(3,7);
...
...
}

## Slide 8: Function Call Conventions: Redux
Our conventions work for simple functions, but they will not handle more complication situations
What do if we have a function with more than two arguments?
What happens if we have a function that calls another function? What if that other function is itself, i.e., recursive function calls?
What do we do with register values that the caller function would like to use after the function call?
int fact(int n) {
if (n < 1)
return 1;
else
return n * fact(n-1);
}

## Slide 9: Stacks
All of these situations can be handled using a data structure called a stack.
A stack is a Last-In, First-Out (LIFO) structure in data memory.
  Typically starts at the largest address in memory and grows toward smaller addresses.
Two basic stack operations:
  Push: Put a value onto the top of the stack
  Pop: Get a value off of the top of the stack
0xFFFF
0x0000
Stack Pointer
(Register X)
top of stack

## Slide 10: Stacks
The function calling convention typically reserves a register for pointing at the top of the stack.
  Extra arguments, return addresses, values to be preserved are put on the stack as part of the function calling process.
The full use of the stack is beyond this course, but a simple example for extra arguments is:
  Caller puts first two arguments in registers.
  Caller pushes remaining arguments onto stack.
  Caller jumps to callee.
  Callee pops arguments off stack as necessary.
  Must ensure that stack pointer is set properly after the function returns.

## Slide 11: The Last Word…
Take ECE 2500 – Introduction to Computer Organization – for more fun with stacks…