## Slide 1: ECE 2504: Introduction to Computer Engineering
Section 2:
Combinational Logic

## Slide 2: Introduction
This section introduces the concepts and techniques central to the design and implementation of digital logic circuits.
The ideas in this section are based on the work of George Boole (1854) and Claude Shannon (1938)

## Slide 3: Binary Logic
Binary logic describes a system where variables can take on one of two values.
Logical operators produce binary outputs based upon their binary inputs and the operation they perform.
Logic gates physically implement these operations. We can combine logic gates in networks to synthesize a desired function.

## Slide 4: Primitive Logic Gates
There are 3 primitive logic functions: AND, OR, and NOT
AND
  The AND function outputs 1 only when all of its inputs equal 1. The function outputs 0 if any of its inputs equal 0.
  Notation: A ∧ B, A • B, AB
  We can use a truth table to define the AND operation for an arbitrary number of inputs.

## Slide 5: Primitive Logic Gates
  This truth table describes the case for the 2-input AND gate.
A | B | AB
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 6: Primitive Logic Gates
OR
  The OR function outputs 1 if any of its inputs equals 1. The function outputs 0 if all of its inputs equal 0.
  Notation: A ∨ B, A + B
  This truth table describes the case for the 2-input OR gate.
A | B | A + B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 7: Primitive Logic Gates
NOT (Inverter)
  The NOT function outputs the complement of the input value.
  Notation: A′,
A | A′
0 | 1
1 | 0

## Slide 8: Primitive Logic Gates
Symbols
AND gate
OR gate
Inverter (NOT gate)

## Slide 9: Functional Completeness
A set of logic gates is functionally complete if any function can be implemented using only gates from the set.
Together, the AND, OR, and NOT gates form a functionally complete set.
Example
f(A,B,C,D) = AB + CD′ + A′BD

## Slide 10: Complementary Logic Gates
NAND
  A NAND gate is an AND gate with its output inverted.
  Therefore, the NAND function outputs 0 only when all of its inputs are 1. The function outputs 1 if any of its inputs equal 0.
  NAND gates are more common in digital circuits than AND gates because they are easier to fabricate.
  The NAND gate is functionally complete by itself.

## Slide 11: Complementary Logic Gates
  This truth table describes the case for the 2-input NAND gate.
A | B | (AB)′
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 12: Complementary Logic Gates
NOR
  A NOR gate is an OR gate with its output inverted.
  Therefore, the NOR function outputs 0 if any of its inputs are 1. The function outputs 1 if all of its inputs equal 0.
  NOR gates are more common in digital circuits than OR gates because they are easier to fabricate.
  The NOR gate is functionally complete by itself.

## Slide 13: Complementary Logic Gates
  This truth table describes the case for the 2-input NOR gate.
A | B | (A+B)′
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 14: Complementary Logic Gates
Symbols
NAND gate
NOR gate

## Slide 15: Other Logic Functions
Exclusive-OR (XOR)
  We can express the 2-input XOR function in terms of primitive logic gates: A⊕B = A′B + AB′
  The XOR gate is NOT functionally complete.
  How do we define the XOR function for more than 2 inputs?

## Slide 16: Other Logic Functions
  This truth table describes the case for the 2-input XOR gate.
A | B | A ⊕ B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 17: Other Logic Functions
Exclusive-NOR (XNOR)
  We can express the 2-input XNOR function in terms of primitive logic gates: A⊗B = AB + A′B′
  Sometimes, the 2-input XNOR functions is called an equivalence function.
  The XNOR gate is NOT functionally complete.
  How do we define the XNOR function for more than 2 inputs?

## Slide 18: Other Logic Functions
  This truth table describes the case for the 2-input XNOR gate.
A | B | A⊗B
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 19: Other Logic Functions
Symbols
XOR gate
XNOR gate

## Slide 20: Boolean Algebra
Boolean algebra provides the theoretical structure for the manipulation of logic systems.
Boolean algebra allows us to relate truth tables and input-output forms to algebraic expressions.
The purpose of Boolean algebra is to give the designer a means to reduce a logical expression to its simplest form.

## Slide 21: Boolean Algebra
A Boolean function is an algebraic expression that contains a set of operators (AND, OR, NOT) and a set of symbols (0, 1)
A Boolean (or binary) variable can take on either symbol value. We can represent input and output signals as Boolean variables.
We can implement Boolean functions using the logic gates that correspond to the functions.

## Slide 22: Boolean Algebra
Axioms of Boolean Algebra
x + 0 = x | x • 1 = x
x + 1 = 1 | x • 0 = 0
x + x = x | x • x = x
x + x′ = 1 | x • x′ = 0
(x′)′ = x | 
x + y = y + x | xy = yx
(x + y) + z = x + (y + z) | x(yz) = (xy)z
x(y + z) = xy + xz | x + yz = (x + y)(x + z)
(x + y)′ = x′y′ | (xy)′ = x′ + y′
Notes: Duality: interchange • and +, and 0’s and 1’s. The result is also true.

## Slide 23: Boolean Algebra
Simplification using Boolean algebra can be time-consuming:
f(A,B) = [A′ • (A + B′)]′
= (A′)′ + (A + B′)′ (17)
= A + (A + B′)′ (9)
= A + A′ • (B′)′ (16)
= A + A′B (9)
= (A + A′)(A + B) (15)
= (1)(A + B) (7)
= (A + B)(1) (11)
= A + B (2)
An important intermediate step of this proof is the derivation of a theorem:
A + A′B = A + B

## Slide 24: Logic Simplification
Our design task is to find the minimal algebraic expression that represents a logic function.
A logic function does not have a unique algebraic expression.
Finding the minimal algebraic expression by applying Boolean algebra to a non-minimal form of the same algebraic expression is tedious and lacks deterministic rules.

## Slide 25: Logic Simplification
literal – A representational form of a variable.
minterm – A product term containing one literal form of each variable in a function.
maxterm – A sum term containing one literal form of each variable in a function.
Notes: For a literal representation A, there are two literal forms. A and A compliment.
Given a boolean function f(A,B,C,D), we will talk about it in the literal forms of those variables that formt he terms that go into the expression
Literals form the basis of minterm and maxterm.
A product term asks what operator we ask to unite the literals. It is an AND gate *
An sum term uses an OR gate +
What units the two are that they are either a product term or a sum term where the product or sum contains a literal form of everyvariable, exactly once
In a four variable function, we can construct terms that satisfy the definitions.
In AB’C’D, it has a literal form for every variable.
Contrast with A’BC . It isn’t a minterm of the function above. IT is missing a literal form of the variable D.
In the same veign. A possible maxterm is A’+B’+C’+D’

## Slide 26: Logic Simplification
The truth table representation of a logic function is unique.
Consider the following truth table:
f(A,B,C) = A′BC′ + A′BC + AB′C′ + AB′C
Minterm list: f(A,B,C) = Σm(2,3,4,5)
Maxterm list: f(A,B,C) = ΠM(0,1,6,7)
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Notes: 8/27/2012: The maxterm form was wrong originally. It had f’ instead of f…
Unlike algebraic expressions, when we express a function in a truth table. The truth table representation is uniqe.
Truth table are the start of logic simplifcations
A truth table is proper and unique.
This truth table allows one to derive an algebraic expression.
In row 3, note how A and C are both 0. But to get a 1 for the F, ALL need to be a 1. This means that A and C need to be inverterd before heading into an AND gate. The B is left alone.
When the output of the function is 1, a combination that causes it is a minterm of the function.
For row 3, it is 010 which is thus 2, for row 4 it is 011 which is 3 and so on. Thus following minterm
For row 1, it is 000 which is 0, and for row 0 it is 001 which is 1, thus following the maxterm list.

## Slide 27: Karnaugh Maps
A Karnaugh map is a diagram made up of squares
  Each square represents one possible minterm of a function.
  The squares are labeled with their minterm number. For example, ABC = 101 is minterm 5.
  We enter a 1 or a 0 into each box of the Karnaugh map based on the function’s output for that literal combination.
Notes: 2 to the power n using n bits.
The boxes are equal to 2 to the power of n.
The first step is to map the section. We put a 0 or 1 based on if it is a min term or maxterm.

## Slide 28: Karnaugh Maps
This is a 3-variable Karnaugh map.
What do you notice about the way that it is labeled?
 |  | BC |  |  | 
 |  | 00 | 01 | 11 | 10
A | 0 | 0 | 1 | 3 | 2
 | 1 | 4 | 5 | 7 | 6
Notes: 2^3 is 8 which is why it has 8 boxes.
Where A equals 1 and BC equals 10 then it is 6 because 110 which is 6
They are in a gray code order. The counting order thus skips around.
The halmark of a karnaugh map is that physica adjacency of boxes coresponds to a quality that we call logical adjacency
Two terms of logically adjacent if they differ by 1 and only 1 value.
They both have the same value for A. See worksheet in class for marked map
We leave variable B out in all its literal forms because they are not the same for every member of the group as it is a 0 and then a 1
A C is in because it has the same value which is 1 and 1
Thus, it is AC without using boolean algebra. The map did it for us.

## Slide 29: Karnaugh Maps
The squares in a Karnaugh map are arranged so that the labels of adjacent squares differ in only one literal.
  Physical adjacency on the map corresponds to logical adjacency of the terms.
  To achieve this, we label the map using Gray code, so that only one variable changes as we move from one box to another.
  We can use the map to recognize patterns of boxes from which we can derive simpler algebraic terms.
Notes: Gotta make a truth table before you make the K map

## Slide 30: Karnaugh Maps
Enter the function into the map.
Group together adjacent squares that contain 1s. The number of boxes in the group must be a power of 2. They must also have mutual logical adjacency.
Maximize the sizes of your groups.
Minimize the number of your groups.
A square can be a member of many different groups. However, each group must contain at least one square that is not in any other group. This ensures that none of the groups are redundant.
Notes: In the series of quizes.
A number of sequential questions wil pertain to carrying out the steps in a separate manner.
First step is to enter the function into the map
If we know what the minterma dn the maxterm are through the truth table or list. We can enter 01 of the map in a way that agrees with the information of the minterm list
Mapping the function pertains to entering info that coresponds to what is given
After mapping. WE can form groups. They are the groups we saw before. Where some number of minterms that exhibit a quality called logical adjacency. Two terms differing by only one value.
There can be multiple minterms that exhibit logical adjacency.
Even if they are not physically adjacent on the map, they can still be depending on what variables are given.
Don’t make groups of 3, 6 or that have a power of 2, you will be forming groups where name describes a member of the set. It’ll look like a sombrero maybe
A minterm can be in more than one group. They can also overlap. You just hve to make sure that the group in the cover is not redundant
Every group needs to have at least one minterm that no other group contains.
Overlapping is not redudnant in itself
All K maps we show him have to be labeeled correctly
Making a group of smallest groups while being maximized
Make sure they are not redundant.

## Slide 31: Karnaugh Maps
Each group in the map represents a product term in a sum-of-products function. Name the group by using the literals that all of the group members have in common.
If two properly-sized groups show logical adjacency, they can be reduced to a larger group having one fewer literal.

## Slide 32: Karnaugh Maps
f(A,B,C) = Σm(2,3,4,5)
Map the function.
Minimize the function.
Name the groups.
Formulate the function.
f(A,B,C) =
 |  | BC |  |  | 
 |  | 00 | 01 | 11 | 10
A | 0 | 0 | 1 | 3 | 2
 | 1 | 4 | 5 | 7 | 6

## Slide 33: Karnaugh Maps
f(A,B,C) = Σm(3,4,6,7)
Map the function.
Minimize the function.
Name the groups.
Formulate the function.
f(A,B,C) =
 |  | BC |  |  | 
 |  | 00 | 01 | 11 | 10
A | 0 | 0 | 1 | 3 | 2
 | 1 | 4 | 5 | 7 | 6

## Slide 34: Karnaugh Maps
f(A,B,C) = A′B + A′C + BC + AB ′C
Map the groups in the function.
Use the minterms you find to minimize the function.
Name the new groups.
Formulate the function.
f(A,B,C) =
 |  | BC |  |  | 
 |  | 00 | 01 | 11 | 10
A | 0 | 0 | 1 | 3 | 2
 | 1 | 4 | 5 | 7 | 6

## Slide 35: Karnaugh Maps
The size of the map doubles each time we add a new variable.
We have to take care to observe new instances of adjacency.
 |  | CD |  |  | 
 |  | 00 | 01 | 11 | 10
AB | 00 | 0 | 1 | 3 | 2
 | 01 | 4 | 5 | 7 | 6
 | 11 | 12 | 13 | 15 | 14
 | 10 | 8 | 9 | 11 | 10

## Slide 36: Karnaugh Maps
Obtain the simplest SOP form of f(A,B,C,D) = Σm(0,1,2,6,8,9,10).
 |  | CD |  |  | 
 |  | 00 | 01 | 11 | 10
AB | 00 | 0 | 1 | 3 | 2
 | 01 | 4 | 5 | 7 | 6
 | 11 | 12 | 13 | 15 | 14
 | 10 | 8 | 9 | 11 | 10
Notes: F = BC comp + BD comp + A comp C D comp

## Slide 37: Karnaugh Maps
Obtain the simplest SOP form of f(A,B,C,D) = Σm(0,1,2,4,5,6,8,9,12,13,14).
 |  | CD |  |  | 
 |  | 00 | 01 | 11 | 10
AB | 00 | 0 | 1 | 3 | 2
 | 01 | 4 | 5 | 7 | 6
 | 11 | 12 | 13 | 15 | 14
 | 10 | 8 | 9 | 11 | 10

## Slide 38: Karnaugh Maps
As the number of variables increases, the patterns of adjacencies can become difficult to find.
To learn techniques involving more variables and multiple output functions, take Digital Design I!

## Slide 39: Karnaugh Maps
So far, we have grouped the minterms (the ones) in our maps. This produces functions in the sum-of-products form.
  These functions have a set of first-level AND gates unified by a second-level OR gate.
  How else can we implement these sum-of-products functions?
    Use double-negation and DeMorgan’s to use only NAND gates

## Slide 40: Karnaugh Maps
An alternative functional representation is the product-of-sums representation.
  These functions have a set of first-level OR gates unified by a second-level AND gate
  How else can we implement these product-of-sums functions?

## Slide 41: Karnaugh Maps
We can use Karnaugh maps to derive the product-of-sums form of a function.
  Map the function as before.
  Group the maxterms (the zeros) of the function in the same way that you grouped the ones previously.
  This yields a minimized expression for f′ in SOP form.
  Complement both sides of the function. Use DeMorgan’s Theorem to derive f in POS form.

## Slide 42: Karnaugh Maps
Obtain the simplest POS form of f(A,B,C,D) = Σm(0,1,2,6,8,9,10).
 |  | CD |  |  | 
 |  | 00 | 01 | 11 | 10
AB | 00 | 0 | 1 | 3 | 2
 | 01 | 4 | 5 | 7 | 6
 | 11 | 12 | 13 | 15 | 14
 | 10 | 8 | 9 | 11 | 10
Notes: If you know where the 1s are, you can then find out where the 0s are.
Then you just group the 0s.
Row 3 can be fully covered horizontally. Column 3 can be wholly covered, and then row 2-23 can be done in with a 4 square cover.
‘\
This is thus f comp = AB+CD+BC comp
Then you complicment both sides
To get regular f equal to (AB comp)*(CD comp)*(B comp *C)
To get another
(A comp+B omp)(C comp + D comp)(B comp + C)

## Slide 43: Karnaugh Maps
Obtain the simplest POS form of f(A,B,C,D) = Σm(0,1,2,4,5,6,8,9,12,13,14).
 |  | CD |  |  | 
 |  | 00 | 01 | 11 | 10
AB | 00 | 0 | 1 | 3 | 2
 | 01 | 4 | 5 | 7 | 6
 | 11 | 12 | 13 | 15 | 14
 | 10 | 8 | 9 | 11 | 10

## Slide 44: Karnaugh Maps
Sometimes a designer doesn’t care whether a particular combination of inputs causes an output of 0 or 1.
Consider the binary-coded decimal codes.
  Only 10 of the 16 four-variable codes represent valid BCD codes. The other 6 codes are invalid.
  If we design a function to accept BCD inputs, it doesn’t matter what the invalid codes produce as outputs, since they will not occur as inputs

## Slide 45: Karnaugh Maps
Literal terms whose outputs do not impact the output function are called don’t care conditions.
  Use “d” or “x” to represent a don’t care in a Karnaugh map.
Functions that contain don’t care conditions are called incompletely-specified functions.
  SOP: f(A,B,C,D) = Σm(0,3,6,9) + d(10, 11, 12, 13, 14, 15)
  POS: f(A,B,C,D) = ΠM(1,2,4,5,7,8) • D(10, 11, 12, 13, 14, 15)

## Slide 46: Karnaugh Maps
To minimize an incompletely-specified function, observe these additional requirements.
  Use don’t cares as 1s or 0s when forming groups of minterms (in SOP functions) or maxterms (in POS functions).
  Use as many of the don’t cares as you need to make larger groups.
  Don’t make groups that are all don’t cares!

## Slide 47: Karnaugh Maps
f(A,B,C,D) = Σm(0,1,2,6,8,9,12,14) + d(4, 5,10,13,15)
 |  | CD |  |  | 
 |  | 00 | 01 | 11 | 10
AB | 00 | 0 | 1 | 3 | 2
 | 01 | 4 | 5 | 7 | 6
 | 11 | 12 | 13 | 15 | 14
 | 10 | 8 | 9 | 11 | 10
Notes: Certain input combos are don’t cares.

## Slide 48: Karnaugh Maps
f(A,B,C,D) = Σm(0,3,6, 9) + d(10,11,12,13,14,15)
 |  | CD |  |  | 
 |  | 00 | 01 | 11 | 10
AB | 00 | 0 | 1 | 3 | 2
 | 01 | 4 | 5 | 7 | 6
 | 11 | 12 | 13 | 15 | 14
 | 10 | 8 | 9 | 11 | 10
Notes: Has sigma to signify Sum
Never do opposing corners.

## Slide 49: Tri-state buffers
Logic gates introduced so far always drive a 0 or 1 on their output
  Cannot connect outputs of multiple gates together
Tri-state buffers can drive a third value—high impedance (hi-Z)
  Hi-Z means no voltage is driven
  Can connect outputs of tri-state buffers together as long as no more than one drives at any time
  When would we want to do that?
Notes: Can be both 0, 1, or high impedence.
As an impedence goes up, the current goes towards 0?
Called a multiplexer

## Slide 50: Tri-state buffers
  Symbol
IN
EN
OUT
EN | In | Out
0 | X | Hi-Z
1 | 0 | 0
1 | 1 | 1

## Slide 51: Tri-state buffers
  Example
Select | A | B | Out
0 | 0 | X | 0
0 | 1 | X | 1
1 | X | 0 | 0
1 | X | 1 | 1
A
Out
B
Select