## Slide 1: ECE 2504: Introduction to Computer Engineering
Section 4:
Arithmetic Functions and HDLs
(Part 1)

## Slide 2: Iterative Combinational Circuits
Arithmetic functions
  Operate on binary vectors
  Use the same subfunction in each bit position
Can design functional block for subfunction and repeat to obtain functional block for overall function
Cell - subfunction block
Iterative array - a array of interconnected cells
An iterative array can be in a single dimension (1D) or multiple dimensions
Notes: Decompose workings into subfunctions that are the same for every bit position.

## Slide 3: Block Diagram of a 1D Iterative Array
Example: n = 32
  Number of inputs = ?
  Truth table rows = ?
  Equations with up to ? input variables
  Equations with huge number of terms
  Design impractical!
Iterative array takes advantage of the regularity to make design feasible
Notes: Number of Inputs = 66
Truth Table Rows = 266
Equations with up to 66 variables
The top boxes are primary inputs
They are described as an operand
If you want to add two 32bit values, you get different stuff
The y inputs are secondary inputs and outputs. The carry is a good example of a secondary I/O

## Slide 4: Iterative design for addition
Approach for a n-bit adder:
  Use the mechanism for binary addition to reduce the complexity of the problem.
  In each column, we add two 1-bit addend to a 1-bit carry-in to produce a 1-bit sum and a 1-bit carry out.
  Decompose the design into the synthesis of n identical 1-bit full adders.
 | 1 | 1 | 0 | 1
+ | 0 | 1 | 0 | 1

## Slide 5: Iterative design for addition
For the 1-bit full adder:
Si = Ai′Bi′Ci + Ai′BiCi′ + AiBi′Ci′ + AiBiCi
= Ai ⊕ Bi ⊕ Ci
Ci+1 = AiBi + AiCi + BiCi
Ai | Bi | Ci | Si | Ci+1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Notes: Value of I doesn’t matter.

## Slide 6: Binary Adders
To add multiple operands, we “bundle” logical signals together into vectors and use functional blocks that operate on the vectors
Example: 4-bit ripple carry adder: Adds input vectors A(3:0) and B(3:0) to get a sum vector S(3:0)
Note: carry out of cell i becomes carry in of cell (i + 1)
Description
Subscript
3 2 1 0
Name
Carry In
0 1 1 0
Ci
Augend
1 0 1 1
Ai
Addend
0 0 1 1
Bi
Sum
1 1 1 0
Si
Carry out
0 0 1 1
Ci+1
Notes: We get a ripple carry adder.

## Slide 7: 4-bit Ripple Carry Binary Adder
A 4-bit Ripple Carry Adder made from four 1-bit Full Adders:
Notes: If C0 was 0, it gets a single bit as the output for S0

## Slide 8: Fixed Point Representation
We have three different methods for expressing signed numbers.
  Signed magnitude
  1’s complement
    Defined as (rn – 1) – N
  2’s complement
    Defined as rn – N
Each method of representation has advantages.
We will choose a method for general use based on its lack of drawbacks
Notes: We need to consider that the use of binary representation of values that are now signed. As it tunrs out, binary has three different ways that we can represent signed numbers.
3 signed thingies.
Particular method
This is due to the lack of drawbacks..
Seen as signed ones and twos compliment.

## Slide 9: Fixed Point Representation
Every n-bit signed number consists of two fields.
The most significant bit is the sign bit. By convention, a number having a sign bit of 0 is positive. A number having a sign bit of 1 is negative.
The remaining n-1 bits tell us something about the size of the number.
Notes: When we talk about an n bit value. We are to imagine that the n bit value is divided into two different fields.
The first field consists soley of the most signifigant bit of the number and called the msb or the most signifigant bit of the number.
It gives us info of the sign of the bit of what we are trying to do.
Easy convention
If the signed bit is 0 then the number is a positive number
If the signed bit is a 1 then it is a negative number

## Slide 10: Signed Magnitude Representation
In a signed magnitude number, the most significant bit is the sign bit.
The remaining bits express the magnitude of the number. Interpret the magnitude just as you would an unsigned binary number.
Example (using 5 bits)
  (+4)10 = 0 0100
  (–4)10 = 1 0100
Notes: The remaining bits are the general number
If we were to add these numbers together using arithmetic
It would come out to be 11000
If we were ot intepret it as signed magnitude, then it would represent negative 8 due to a signed bit of 1 and a value of 1000 for the rest.

## Slide 11: Signed Magnitude Representation
Features
  This representation looks like the method that we use to represent signed numbers in radix-10.
  Arithmetic in signed magnitude is “complex” because we need to compare the signs of the numbers before doing the arithmetic.
  There are two representations for zero.

## Slide 12: Signed 1’s Complement Representation
An inverter performs the complement operation.
We can use the complement operation to produce the 1’s complement operation.
Example
The 1’s complement of 00100 is 11011.
A | A′
0 | 1
1 | 0

## Slide 13: Signed 1’s Complement Representation
In the signed 1’s complement representation, two numbers have opposite value if their codes are 1’s complements of each other.
Remember, a number having a sign bit of 0 is positive. A number having a sign bit of 1 is negative.
Example (using 5 bits)
00100 = +4
11011 = –4

## Slide 14: Signed 1’s Complement Arithmetic
1’s complement arithmetic is simpler than signed magnitude arithmetic.
  Add the two numbers. Make sure that both numbers re expressed in 1’s complement representation
  If there is a carry-out of the most significant bit (the sign bit), increment the result.
  Discard the carry-out. The result must have the same precision as that of the addends.

## Slide 15: Signed 1’s Complement Representation
Features
  Notice that positive numbers are the same in the signed 1’s complement representation as they are in the signed magnitude representation.
  Notice that negative numbers generally look different in the two representations.
  There are still two representations of zero.

## Slide 16: Signed 2’s Complement Representation
To perform the 2’s complement operation, first perform the 1’s complement operation, then increment the result.
There are short-cut methods for performing the 2’s complement operation.
Example
The 2’s complement of 00100 is 11100.

## Slide 17: Signed 2’s Complement Representation
In the signed 2’s complement representation, two numbers have opposite value if their codes are 2’s complements of each other.
Remember, a number having a sign bit of 0 is positive. A number having a sign bit of 1 is negative.
Example (using 5 bits)
00100 = +4
11100 = –4

## Slide 18: Signed 2’s Complement Arithmetic
Addition
  Add the two numbers. Make sure that both numbers re expressed in 2’s complement representation
  Discard the carry-out. The result must have the same precision as that of the addends.
Subtraction
  By definition, a – b = a + (-b)
  Take the 2’s complement of the subtrahend, then add.

## Slide 19: 2’s complement vs. dedicated subtractor
Subtractor/adder:
2’s complement adder:
Notes: Wether or not S is 0 or S is 1 in the 2s compliment adder. Then A will be that.
Since S is connected directly to the carry in. .

## Slide 20: Signed 2’s Complement Representation
Features
  Notice that positive numbers are the same in all three formats. We use this fact to provide a common starting point for deriving negative numbers.
  Notice that negative numbers generally look different in all three formats.
  The signed 2’s complement representation has a unique representation for 0. This means that we can derive 2n unique n-bit numbers

## Slide 21: Integer Overflow
Using a particular n-bit signed 2’s complement representation limits the number of integers that we can express.
Sometimes, we cannot use n bits to represent the result of an arithmetic problem that uses n-bit operands

## Slide 22: Integer Overflow
Example
The problem here is overflow. We cannot interpret the result as the correct result of the addition problem.
What are the indicators of overflow?
 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | = +64
+ | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | = +100

## Slide 23: Integer Overflow
Overflow cannot occur in an addition problem if the numbers have different sign bits.
If overflow occurs, a computer system should go to an error checking routine. Overflow detection is typically a hardware problem. Overflow correction is typically a software problem.

## Slide 24: Floating Point Representation
Fixed point representations lack sufficient range and precision for most scientific calculations.
We can use a floating point representation that involves an exponential notation.
The value of the number is
m  re
where m is the mantissa, r is the radix, and e is the exponent.

## Slide 25: Floating Point Representation
In scientific notation, we assume a radix of 10. This means that the mantissa and exponent are sufficient to represent a unique number to a particular precision.
In binary floating point notation, we assume a radix of 2.
Just as in scientific notation, we must follow certain rules to correctly represent the mantissa and the exponent.

## Slide 26: Floating Point Representation
The mantissa of a floating point number represents a signed binary fraction. We assume that all of the bits of place are to the right of a radix point.
The exponent of a floating point number represents a signed integer.
In the simplest case, use signed magnitude representation to express the numbers.

## Slide 27: Floating Point Representation
In non-zero numbers, the mantissa of a floating-point number must be normalized. This means that the most significant bit of the mantissa must be 1.
Example The mantissa .00100101 is not normalized. The mantissa .10010100 is normalized.

## Slide 28: Floating Point Representation
The number of bits in the mantissa determines the number’s precision.
The number of bits in the exponent determines the range.
The standard way to represent zero is to set the mantissa and exponent (including their sign bits) to zero.

## Slide 29: IEEE 754 Floating Point Representation
IEEE has defined standard formats for 32-bit and 64-bit floating point numbers.
These formats employ a signed offset exponent and a fractional mantissa with an understood 1.
The qualities, along with allowances for denormalized mantissas, permit a wide range of representation, including non-standard values such as NaN and Infinity.

## Slide 30: IEEE 754 Floating Point Representation
32 bits (single precision)
  1 sign bit, 23-bit mantissa, 8-bit exponent.
  The format has a positive and negative range of 1.401 × 10-45 (denormalized) to 3.402 × 1038.
64 bits: (double precision)
  1 sign bit, 52-bit mantissa, 11-bit exponent.
  The format has a positive and negative range of 4.941 × 10-324 (denormalized) to 1.798 × 10308.

## Slide 31: Other Arithmetic Functions
Convenient to design the functional blocks by contraction - removal of redundancy from circuit to which input fixing has been applied
Functions
  Incrementing
  Decrementing
  Multiplication by Constant
  Division by Constant
  Zero Fill and Extension

## Slide 32: Design by Contraction
Contraction is a technique for simplifying the logic in a functional block to implement a different function
  The new function must be realizable from the original function by applying rudimentary functions to its inputs
  Contraction is treated here only for application of 0s and 1s
  After application of 0s and 1s, equations or the logic diagram are simplified

## Slide 33: Design by Contraction Example
Contraction of a ripple carry adder to an incrementer for n = 3 bits
  Set operand B = 001
  The middle cell can be repeated to make an incrementer with n > 3.

## Slide 34: Incrementing & Decrementing
Incrementing
  Adding a fixed value to an arithmetic variable
  Fixed value is often 1, called counting (up)
  Examples: A + 1, B + 4
  Functional block is called incrementer
Decrementing
  Subtracting a fixed value from an arithmetic variable
  Fixed value is often 1, called counting (down)
  Examples: A - 1, B - 4
  Functional block is called decrementer

## Slide 35: Multiplication/Division by 2n
Multiplication by 100: shift left by 2
Division by 100: shift right by 2 (This also preserves the remainder.)
B
0
B
1
B
2
B
3
C
0
C
1
0
0
C
2
C
3
C
4
C
5
(a)
B
0
B
1
B
2
B
3
C
0
C
2
1
C
2
2
C
1
C
2
0
0
C
3
(b)

## Slide 36: Zero Fill
Zero fill - filling an m-bit operand with 0s to become an n-bit operand with n > m
Filling usually is applied to the MSB end of the operand, but can also be done on the LSB end
Example: 11110101 filled to 16 bits
  MSB end: 0000000011110101
  LSB end: 1111010100000000

## Slide 37: Extension
Extension - increase in the number of bits at the MSB end of an operand by using a complement representation
  Copies the MSB of the operand into the new positions
  Positive operand example: 01110101 extended to 16 bits: → 0000000001110101
  Negative operand example: 11110101 extended to 16 bits: → 1111111111110101

## Slide 38: Terms of Use
All (or portions) of this material © 2008 by Pearson Education, Inc.
Permission is given to incorporate this material or adaptations thereof into classroom presentations and handouts to instructors in courses adopting the latest edition of Logic and Computer Design Fundamentals as the course textbook.
These materials or adaptations thereof are not to be sold or otherwise offered for consideration.
This Terms of Use slide or page is to be included within the original materials or any adaptations thereof.