## Slide 1: ECE 2504: Introduction to Computer Engineering
Section 5: Sequential Circuits

## Slide 2: Sequential Logic
Sequential circuit elements have outputs that depend on the current inputs and on the previous inputs.
The history of the inputs is held in the circuit’s state.
The next state of the circuit depends on the present state and the present input.
The state of the circuit is held in memory devices called flip-flops.

## Slide 3: The SR Latch
An SR latch consists of 2 cross-connected NAND gates or NOR gates.
Latches operate asynchronously. This means that any time that a latch input changes, the latch state can change.
We will consider the SR latch’s characteristic information. which defines the next state as a function of the inputs and the state.
Notes: SR latch is a particular flavor of the sequential element that we call latches.
See notebook lecture mar 30 for diagram
Where some gates output is the other gates input. They work asynchronously.
Wheneever I make a change to one of the inputs. Then the change of the state will be in conjunction to the input state.
A latch = flip flop
When an input combonation is present on the inputs, then the output will make an appropriate change in conjunction with the input change.
It is the premise of characteristi finformation. Where we ask, what is thenext state ofa SR latch be for all possible combinations of Q+ = f(Q,S,R) where we ask what the present sate, present S and present R are going to do to the Q+. Where what happens in the future coorelates to what happens now.
We can think of the S input as a indication that we would like to ‘set’ the input of the latch.
Then the
All that we are required for it to be called a set is to set the state to 1. It is always being set to 1.
R input stands for R(eset)
Reset latch represents specific state change where value becomes 0. It always being set to 0.

## Slide 4: The SR Latch
Rather than consider each separate combination of input and present state, we will consider combinations of inputs that impose certain functions on the next state.
Function | S | R | Q | Q+
No change | 0 | 0 | 0 | 0
Q+ = Q |  |  | 1 | 1
Reset | 0 | 1 | 0 | 0
Q+ = 0 |  |  | 1 | 0
Set | 1 | 0 | 0 | 1
Q+ = 1 |  |  | 1 | 1
Invalid | 1 | 1 | 0 | ×
Q+ = ? |  |  | 1 | ×
Notes: When all is brought into the pic. Instead of having to remember multiple cobminations of Q S and R, t hen we can summarive it here.
They are un ambiguous indicators of how it should behave.
If I am not telling the latch to set its state, and not telling it to Set or RESET , then there will be no change in the latches state. It will just be equal to each other.
When S0 and R is 1. We are telling it to reset its state as R = 1. thus we know that Q+ next wil be all set to 0.
In the fourth case. Bad things happen. If we try to tell it that we want both of them. It is thus an invalid case
Just don’t do it. Don’t apply both at the same time.
Particular values of S and R cause changes to the state where Qs value is unknown at the start of operation. Lets imagine what I write on the note book.
The flip flop circuit is an indication of what is happening now. But the future will be the rpeseent at some point in time. Rgith around here, we can look forward and see that R is 1 when S is 0 at the second invertval. That state of change occurs at a point of time.
At the third invertval, the world blows up because both S and R are equal to 1.

## Slide 5: The SR Flip-Flop
Asynchronous operation is not generally a good design practice. It can be difficult to predict how the circuit will operate.
We can avoid asynchronous operation by using synchronous circuit elements.
We achieve synchronization by adding a new control input to the latch called a clock.
Notes: Since asynch isnt good. We do synchronous operation by using a clock or timing to tell it when to do something.
A

## Slide 6: The SR Flip-Flop
A flip-flop can only change state on the occurrence of an “appropriate” portion of the clock signal
  Rising-edge (or positive-edge): the flip-flop changes state when the clock signal rises from logic-0 to logic-1.
  Falling-edge (or negative-edge): the flip-flop changes state when the clock signal falls from logic-1 to logic-0.
  Level – the flip-flop changes state when the clock signal remains steady at logic-1 for some amount of time.
Notes: A flip flop will only change state when something happens in the clock signa.
Rising edge flip flops have a chnageable state only when the cock is going from 0 to 1. That point in time it goes from 0to 1.
Only those inputs that happen at specific points in times will be utilized and the rest are forgotten by the computer.
Hallmark of sychronous circuits. Putting them in preset fhen adding a clock value to it is recommended.
d

## Slide 7: The D Flip-Flop
Connect an inverter to the R input of an SR flip-flop, then connect the S input to the inverter input.
Call the new input D.
Notice that Q+ = D. The state of the D flip-flop after the clock pulse equals the value on the D input before the clock pulse.
D flip-flop is the most commonly used in today’s technology
Function | D | Q | Q+
Reset | 0 | 0 | 0
Q+ = 0 |  | 1 | 0
Set | 1 | 0 | 1
Q+ = 1 |  | 1 | 1
Notes: Flip flop requires us to remember that where there is a value on the d input that it will take a clock trigger for that flip flop that is on the input and register it on the output. Until that happens, it is possible to have a state of the output that matches out to in because a clock trigger event has not yet happened.
One clock period is not a lot at the moment but we will be able to use the flip flop to design devices

## Slide 8: Other Flip-Flops: The JK Flip-Flop
Imagine that the JK flip-flop improves on the SR flip-flop by not having the invalid case where S = R = 1.
Function | J | K | Q | Q+
No change | 0 | 0 | 0 | 0
Q+ = Q |  |  | 1 | 1
Reset | 0 | 1 | 0 | 0
Q+ = 0 |  |  | 1 | 0
Set | 1 | 0 | 0 | 1
Q+ = 1 |  |  | 1 | 1
Toggle | 1 | 1 | 0 | 1
Q+ = Q′ |  |  | 1 | 0
Notes: D flip flop is more awesome than the JK flip flop so thweatt doesn’t talk about this as much
Flip flop without a clock is a latch

## Slide 9: Other Flip-Flops: The T Flip-Flop
Connect the inputs of a JK flip-flop together to make a single input.
Call the new input T
Function | T | Q | Q+
No Change | 0 | 0 | 0
Q+ = Q |  | 1 | 1
Toggle | 1 | 0 | 1
Q+ = Q′ |  | 1 | 0
Notes: T flop
Think of as a fk flip flop but both its inputs tied together
Able to do the two functions by the jk function by both being 0 or both being 1
When t is 0 it will not go through a change
If t is 1, it will toggle the things.

## Slide 10: Standard Symbols for Storage Elements
Latches
Edge-Triggered Flip-Flops
D with 0 Control
S
R
SR
SR
S
R
D
C
D with 1 Control
D
C
Q
Q’
Q
Q’
Q
Q’
Q
Q’
Positive edge- triggered D
D
C
Negative edge- triggered D
D
C
Q
Q’
Q
Q’

## Slide 11: Direct Inputs
At power-up or at reset, all or part of a sequential circuit usually is initialized to a known state before it begins operation
This initialization is often done outside of the clocked behavior of the circuit, i.e., asynchronously.
Direct R and/or S inputs that control the state of the latches within the flip-flops are used for this initialization.
For the example flip-flop shown
  0 applied to R resets the flip-flop to the 0 state
  0 applied to S sets the flip-flop to the 1 state
D
S
R
Q
Q’

## Slide 12: Flip-Flop Excitation
Characteristic information answers the question “Given the inputs and the present state, what will the next state be?”
In sequential design problems, we typically know the present state and the next state. We need to know the input combinations that cause the desired state change.
We can rearrange the characteristic information to derive excitation information.

## Slide 13: Flip-Flop Excitation
SR flip-flop
D flip-flop
Function? | Q | Q+ | D
 | 0 | 0 | 
 | 0 | 1 | 
 | 1 | 0 | 
 | 1 | 1 | 
Function? | Q | Q+ | S | R
 | 0 | 0 |  | 
 | 0 | 1 |  | 
 | 1 | 0 |  | 
 | 1 | 1 |  | 

## Slide 14: Flip-Flop Excitation
JK flip-flop
T flip-flop
Function? | Q | Q+ | J | K
 | 0 | 0 |  | 
 | 0 | 1 |  | 
 | 1 | 0 |  | 
 | 1 | 1 |  | 
Function? | Q | Q+ | T
 | 0 | 0 | 
 | 0 | 1 | 
 | 1 | 0 | 
 | 1 | 1 | 

## Slide 15: Counter Example
Design a synchronous sequential circuit that counts in 2-bit Gray code. The circuit should only count when input x = 1; if x = 0, the circuit should stay in its current state. Use D flip-flops.
How many states are there?
How do the states advance from one to another?

## Slide 16: Sequential Circuit Design
The behavior of a sequential circuit is governed by the flip-flop’s inputs and its states.
We can represent this information in a state table or a state diagram.
A state table is a truth table that shows all combinations of input and present state, and the next state for each combination.
A state diagram describes the sequential circuit’s behavior with circles for the state, and directed arcs for state transitions
For small circuits, state diagrams are usually easier to understand than tables, but diagrams get complex for large numbers of states
Notes: occ

## Slide 17: Sequential Circuit Design
We use excitation information to determine how each state transition occurs. Then, we represent each excitation input as a function of the variables of the total present state – that is, the inputs and the flip-flop states.
Notes: occ

## Slide 18: Sequential Circuit Design
General Design Procedure
  Model the state machine’s behavior using a state diagram.
  Using the state diagram, generate a state table.
  Simplify the state table. (Take DD I to learn techniques for state reduction.)
  Determine the number of flip-flops you need to implement the state machine.
  Make a state assignment. (DD I presents general and advanced techniques.)

## Slide 19: Sequential Circuit Design
  Choose the flip-flop type.
  Extend the state table to include the excitation information.
  Use Karnaugh maps to derive simplified equations for the flip-flop inputs (the excitation equations) and the circuit outputs, if any exist.
  Simulate the circuit to verify your design.
  Build the circuit and test it until it operates without errors.

## Slide 20: More on State Assignment
Each of the m states must be assigned a unique code.
Minimum number of bits required is n such that n ≥ log2 m
There are (2n – m) unused states.
There are other useful state assignments that use more than the minimum number of bits.

## Slide 21: General Design Example
Design a synchronous sequential circuit that tracks the number of consecutive 1s that occur on an input line, x. For every series of four consecutive 1s, an output z becomes 1. Use D flip-flops.
How many states are there?
How do the states advance from one to another?
Take Digital Design I!

## Slide 22: Terms of Use
All (or portions) of this material © 2008 by Pearson Education, Inc.
Permission is given to incorporate this material or adaptations thereof into classroom presentations and handouts to instructors in courses adopting the latest edition of Logic and Computer Design Fundamentals as the course textbook.
These materials or adaptations thereof are not to be sold or otherwise offered for consideration.
This Terms of Use slide or page is to be included within the original materials or any adaptations thereof.